## Slide 1: A digital twin that warns of glucose spikes early
Phase-1 proof of concept: clinic records plus wearable data, two hours of notice. Built for the Happiest Health Digital Twin Challenge.
One demo patient, 48 hours of glucose. Dashed line = 180 mg/dL. Yellow ring = model alert. Synthetic data.

## Slide 2: Join who the patient is with what is happening now
Clinic record (EHR)
Who the patient is: age, BMI, HbA1c, kidney function, genetic risk markers
Wearable stream
What is happening now: glucose, heart rate, heart-rate variability, sleep, steps
Early warning
An alert about 2 hours before glucose goes above 180 or climbs fast
+
=
The twin is a model of one patient that updates with every new reading and forecasts what comes next.

## Slide 3: How the project works, from raw data to dashboard
1
Generate data
Synthetic clinic records and wearable streams for 500 patients
data/
2
Build features
Trailing windows only, so nothing from the future leaks in. Label: spike in next 2 h
feature_engineering
3
Train and test
Gradient-boosted model, scored with patient-grouped cross-validation
train_model
4
Export results
Risk scores, alerts and explanations for six demo patients
export_dashboard_data
5
Console
Offline web dashboard that shows roster, streams and alerts
dashboard/
Every number in the repo's reports is generated from one metrics file, never typed by hand.

## Slide 4: What the model sees, and what counts as a spike
500
virtual patients
21 days
of readings each, every 15 minutes
1.0 M
patient-moments (rows) to learn from
1.8%
of moments are followed by a spike
A spike means, within the next 2 hours:
30-minute smoothed glucose passes 180 mg/dL
or it rises by 30 mg/dL or more
Smoothing matters: an earlier version fired on sensor noise
Inputs: 12 clinic fields and 5 wearable signals

## Slide 5: One model, tested the hard way
The model
Gradient-boosted decision trees
Learns from the clinic record and the live signals together
Same settings reused for a second, week-ahead heart-strain target
The testing rules
A patient's rows are never in both train and test
Five repeated splits, 25% of patients held out each time
Significance judged across patients, not across folds
Every claim paired with a control that could disprove it

## Slide 6: Headline: a useful signal, and an honest number
0.843
ROC-AUC, averaged over five independent data draws (plus or minus 0.021)
~1 a day
alerts per patient when the alert budget is set to 1% of moments
4 in 10
of those alerts are real spikes (precision 0.41), about 14x better than chance
This is the average, not the best run. The shipped model scored 0.876, which was the luckiest of the five draws, and we say so.

## Slide 7: Wearable signals are what lift the score
Chart: ROC-AUC by feature set (axis starts at 0.70)
| Clinic record only | Shortcut control | Wearable only | Full model (both)
ROC-AUC | 0.823 | 0.854 | 0.871 | 0.876
Shortcut control = clock + current glucose + trend + baseline labs
Full model beats it by +0.022 (p < 0.001)
Heart-rate variability, sleep and activity give +0.017 of that
The gain holds in all 5 data draws
Chart shows the shipped data draw

## Slide 8: What the model leans on most
Chart: Share of the model's decision weight (%)
| Glucose variability (3 h) | HRV right now | BMI | HbA1c | Age | Glucose average (3 h) | Time of day | HRV average (3 h)
Share of importance (%) | 4.5 | 4.7 | 6 | 6.3 | 7.1 | 10.9 | 15 | 15.3
About two-thirds of the weight sits on live wearable signals
Heart-rate variability (HRV) is the single top signal
Time of day is down from 29% in v2 to 15%, no longer the main shortcut
Clinic fields like age and HbA1c still add a steady base

## Slide 9: We tried to break our own result
0.495
Shuffled labels
Scrambling who spiked drops the score to a coin flip, so the pipeline is not leaking answers.
0.802
Same patient, shuffled timing
Knowing who the patient is gives most of the score. Their current state adds about +0.06 on top.
0.82 to 0.88
Five data draws
The score moves with the draw, so we quote the average rather than the best run.
A score is only believable once the shortcuts have been tested and the numbers still stand.

## Slide 10: Does combining both streams pay off? Mixed
+0.053
vs clinic record alone
Clear win (p < 0.001)
+0.022
vs shortcut control
Clear win (p < 0.001)
+0.005
vs best non-fusion mix
Not significant (p = 0.18) and negative in 4 of 5 data draws
Our read
Both streams carry signal, and the model uses it. But fusing everything is not proven better than the best single-stream mix. We report it as a negative finding.
The 'best non-fusion mix' was assembled after seeing the results, so even +0.005 flatters fusion.

## Slide 11: Real data: the code works, the gain shrinks
Run: UCI Diabetes
70 real patients with type 1 diabetes, 50 scored
Same code ran unchanged on real data
Gain over naive baseline: +0.006 (p < 0.001), about 4x smaller than synthetic
AUC of 0.98 is not comparable: 54% of moments are spikes and the naive baseline already scores 0.977
Pending: BIG IDEAs Lab
16 prediabetic adults with glucose, wearable and clinic table for the same people
The one cohort that can test fusion properly
Downloader, converter and checks are built, but only 6 of 16 are downloaded
The paired test has not been run, so no number is quoted

## Slide 12: The clinician console
Six virtual patients, picked by a clinical rule set in advance
Roster with live risk levels
Glucose, heart-rate and HRV streams with real spikes marked
Alert feed and a per-feature explanation of each score
Runs offline, with a clear synthetic-data, not-for-clinical-use banner
Chart: Patient P100133: 48 hours of glucose (synthetic)
A conceptual front end over precomputed output. Not a live system.

## Slide 13: Scores fell as our checks got stricter
v1
0.986
One clinic field (diabetes diagnosis) did the work: 82% of the weight
Caught by the same-patient label shuffle
v2
0.953
The answer was hidden in the meal clock: time of day alone gave 29%
Caught by the shortcut baseline
v3
0.843
Labels fixed, controls added, five-draw average, tests and CI in place
The number we stand behind
A high AUC is not evidence of a good model until a shortcut baseline has been run against it.

## Slide 14: What the project delivers
End-to-end pipeline
Data, features, model, reports and console all run from five commands
Working predictor
0.843 ROC-AUC with a 2-hour warning, calibrated risk scores
Wearables proven useful
+0.022 over a clock-and-glucose shortcut, in 5 of 5 data draws
Honest evaluation kit
Leakage tests, seed sweep, patient-level significance, alert budgets
Real-data protocol
Ran unchanged on 70 real patients; second cohort wired up
Reproducible and open
Tests, CI and MIT licence; no raw real data committed

## Slide 15: What is not proven yet, and what comes next
Not proven yet
Synthetic data is not real physiology
Fusion benefit is untested on real paired data
Much of the score comes from who the patient is, not their current state
Week-ahead heart-strain target is weak (AUC 0.64)
Console is a static demo: no login, audit trail or drift checks
Next steps
1
Run the BIG IDEAs paired fusion test
2
Find CGM-grade real data with a matching clinic record
3
Tune alert thresholds per patient
4
Add login, audit logging, alert-fatigue and drift monitoring